## Slide 1
Budget Conscious Horizontals
In The Big Lime $$$$
Charter Oak Production Co., LLC
Oklahoma City, OK
AADE Symposium
Norman, Oklahoma
13 September 2022

## Slide 2
What is the Big Lime?

## Slide 3
What is the Big Lime?
Clean carbonate (Limestone)
Can have highly porous interval
Pennsylvanian (Marmaton) age
AKA 1st Oswego
Present in N Central Oklahoma
Porosity can be oolitic
Often oil saturated

## Slide 4
The Big Lime?

## Slide 5
Location Of Perry Lake Project
Noble County
Oklahoma City

## Slide 6: Big Lime Type Log Yarbrough #1 Section 36-21N-2W
20% Porosity

## Slide 7
Big Lime Early Production
Four Big Lime Laterals
Completed Mid-2017
Cased, Cemented, Frac’d
IP 180: 800 BOPD
IP 360: 450 BOPD
Two Big Lime Laterals
Open Hold Acid Job – Not Frac’d
Completed 2004
IP’s: 302 & 960 BOPD

## Slide 8: Nadel & Gussman-Wagner #1 Vertical 3500 Gallons 15% HCL IP: 51 BOPD with 37 MCF/D
86,496 BO and 113 MMCF Since 06/1985

## Slide 9: Nadel & Gussman-Perry Lake 1-31H Single 7000 Gallons 20% HCL Open Hole IP: 302 BOPD with 220 MCF/D
73,767 BO and 68 MMCF Since 02/2004

## Slide 10: Nadel & Gussman-Perry Lake 2-31H Single 8500 Gallons 20% HCL Open Hole IP: 960 BOPD with 383 MCF/D
52,529 BO and 66 MMCF Since 12/2004

## Slide 11
Perry Lake Big Lime Structure

## Slide 12
Perry Lake Big Lime Net Pay

## Slide 13: Big Lime Reservoir Properties
Effective Porosity from 18-24%
Water Saturation Approximately 20%
Net Pay from 8 to 14 Feet
Pore Pressure Gradient of 0.433 psi/ft
Milidarcy Range Permeability
GOR 1200 SCF/BBL, BTU = 1260
Oil Gravity = 40 API
Clean Limestone Lithology
Approx 4500’ TVD

## Slide 14: Perry Lake Big Lime Economics
5.7MMBO In-Place Per Section
4 Well Development Per Section
215 MBO Primary EUR per Well
360 MMcf Primary per Well
Currently $3.3MM/Well D&C Cost
Secondary Recovery = 400 MBO per Section?

## Slide 15: Gleason 1-31-30 XH Geosteering Plot

## Slide 16: Gleason 1-31-30 XH Oil Tracers vs Porosity

## Slide 17: Perry Lake 5000’ Lateral Type Curve Projected IP: 200 BOPD with 250 MCF/D
EUR: 215 MBO and 264 MMCF

## Slide 18
Perry Lake Big Lime Drill Rate

## Slide 19: Cost Savings Items
Smaller rig has move and rig up efficiency
Lower pad costs for smaller rig
Fresh mud system
Soil farm mud adjacent to pad
Lower water costs due to proximity to lake
Use of conventional directional vs RSS
Use of alternate surface/intermediate casing
Savings in tapered casing string

## Slide 20: Perry Lake Casing Cost Savings (One Mile Lateral)
Surface: 350’ of 10 ¾” @ $50/ft vs 13 3/8” @ $88/ft results in $13,300 savings
Intermediate: 5000’ of 7 5/8” @ $45/ft vs 9 5/8” @ $90/ft results in $225,000 savings
Production: Tapered string of 5 ½” to 4 ½” with 5000’ of 4 ½” @ $24/ft vs 5 ½” @ $34/ft results in $50,000 savings
Total casing savings = $288,300

## Slide 21: Budget Conscious Lateral Summary
Drilling costs are approx $1MM for one mile lateral
Total well costs slightly over $3MM (Note that frac is over $1MM)
Current ROI is high double digits at BOKF strip pricing with 3X undiscounted return
Most significant savings from alternate casing program without use of a liner
Watching the small items can add up, just don’t step on $100 bills to pick up a dime!