## Slide 2
Solution:
Laserstream, LP with the BEMISTM system measures the ID and Ovality of Casing to .002” inch – End to End. This data, along with full length UT data, will allow an inventory of pipe to be sorted into groups based on physical characteristics. Properties of each group can be quantified by collapse testing.
Problem: API Collapse is based on minimums, potentially a higher collapse could be used to design wells.

## Slide 3
Phase 1: Data Collection
Heat and Batch (Yield)
ID Profilometry for min/max/average ID (Ovality)
Full Length UT to obtain min/max/average wall (Eccentricity)
  may have been performed during receiving inspection

## Slide 4
Laser ID Profilometry
BEMIS™ Pipe Scanner
Adjustable scan head

## Slide 5
Threads and Ovality
9 7/8” CSG

## Slide 6
ID Stats of 9 7/8” CSG
Book Value = 8.625”
Actual = 8.778”
Distance from Pin
8.778” - 8.625” = .15”

## Slide 7
Actual pipe wall
Reference Surface
Radial Cursor Measures Difference
Laser Measurement of Ovality

## Slide 8
Pipe Out of Round for Short Section

## Slide 9
Distance from Pin
Distance from Pin

## Slide 10
ID Variance Provided Every Inch Over the Length of the Joint
Note: Exact ID for Cement Displacements, Max ID for Packer Setting Integrity, and Caliper Baseline

## Slide 11
Phase 2: The ID Data Would be Entered Into a Tally Sheet, with Wall Thickness Data, and Collapse Calculated
Joint # | AVERAGE ID ENTIRE JOINT | AVERAGE ID VARIANCE | MAX ID VARIANCE | MIN WALL | ECCEN-TRICITY | Length | BBLs/jt | Calculated Collapse
57 | 12.464 | 0.21% | 0.70% | 0.708 | 14 % | 41.8 | 6.3082 | 7255
58 | 12.378 | 0.25% | 0.89% | 0.67 | 12% | 44.2 | 6.5787 | 7585
59 | 12.489 | 0.24% | 1.10% | 0.68 | 13% | 38 | 5.7578 | 7047
Klever–Tamano equations can be used to estimate collapse based on actual characteristics.
#57

## Slide 12
Phase 3: Pipe is Grouped Based on Estimated Value
Joint # | Group Number | AVERAGE ID ENTIRE JOINT | Length | Calculated Collapse
58 | A | 12.378 | 44.2 | 7585
60 | A | 12.337 | 44.5 | 7430
57 | A | 12.464 | 42.8 | 7255
61 | A | 12.443 | 41.3 | 7135
56 | B | 12.389 | 43.4 | 7077
59 | B | 12.489 | 38 | 7047
Joints that meet a set criteria would be given a certain Grouping (A, B, C). The lowest value in the grouping would be sent for collapse testing.
For example: Group A is sorted as everything that calculates greater than 7100 psi. Therefore joint #61 would be sent for collapse testing.

## Slide 13
Phase 4: Collapse Testing to Be Done Per API TR 5C3
Collapse Testing to be performed on specimens for each grouping.
Minimums for each grouping established.
Tally would be designed to place pipe for optimized string performance.

## Slide 14: What else can Laserstream Do?

## Slide 15: CRA Tubing / VIT

## Slide 16: CRA Tubing

## Slide 17: Risers
Laser scan image and measurement of wall loss
Note: linear position and azimuthal position

## Slide 18: LaserViewer 3D™ Visualization/ Analysis Software
Wireline Gouge under threads
Coil Tubing Wear and
Wireline gouges

## Slide 19
Progressive Cavity Stator
ID Scan

## Slide 20: Cross Section Rifled Barrel
The cross section tab displays a scaled
two-dimensional cross-section of the scan data.

## Slide 21
Scott King – 281-883-3697
jscott.king@laserstreamlp.com
Jason Waligura – 713-775-4455
jason.waligura@laserstreamlp.com